1996 Mitsui Seiki HT 3A

- Travel

  - X-Axis: 21.6”

  - Y-Axis: 19.68”

  - Z-Axis: 19.68”

  - B-Axis Indexing: 0.001º

- Traverse Rate

  - X-Axis: 945 IPM

  - Y-Axis: 945 IPM

  - Z-Axis: 945 IPM

- Spindle Speed: 12,000 RPM

- Spindle Motor: 20HP

- Spindle Taper: CAT 40

- Tool Capacity: 90

- Maximum Tool Weight: 22lbs

- Maximum Tool Length: 11.81”

- Number of Pallets: 2

- Pallet Change Time: 6 Seconds

- Spindle Nose to Pallet Changer: 4.72”-24.4”

- Spindle Center to Pallet Top: 5.9”-25.59”

- Pallet Load Capacity: 880lbs

- Dimensions: 129” x 195” x 108”

- Machine Weight: 22,100lbs

Equipped With:

- Fanuc 15-M Control with 14” Color CRT Screen

- RS232 Port

- Fully Enclosed Guards

$14,500.00

Balance Due By Cashiers Check Before Pick Up

Shipping Buyer is Responsible for All Freight & Rigging

Contact: Steve Norcio 410 750 1130 or at snorcio@mtacompanyinc.com