Hardinge CHNC I with Fanuc Control

- Swing over bed: 14”

- Maximum Turning Diameter: 8”

- Maximum Fixture Diameter: 9”

- X-Axis Travel: 4.5”

- Y-Axis Travel: 12”

- Rapid Traverse (X-Axis): 200 IPM

- Rapid Traverse (Z-Axis): 400 IPM

- Spindle Nose: A2-5”

- Spindle Bore: 1.875”

- Maximum Bar Capacity: 1.625”

- Spindle Speed: 50-5,000 RPM

- Spindle Motor: 10 HP

- Tool Capacity: 8 Stations

- Tool Change Time: 1-2 seconds

- Weight: 8000 lbs

- RS232 Interface

$3,500.00

Balance Due By Cashiers Check Before Pick Up

Shipping Buyer is Responsible for All Freight & Rigging

Contact: Steve Norcio 410 750 1130 or at snorcio@mtacompanyinc.com