1986 Matsuura MC 800 V Yasnac MX1 Control

Travel: X-Axis 31.5"

Y-Axis: 17.32"

Z-Axis: 19.09"

Table Size: 45" x 16.14"

Spindle Speed: 25 - 4500 RPM

Spindle Taper: BT 40

Spindle Nose to Table Top: 6.89" - 26.97"

Spindle Motor: 10 / 7.5 HP AC

Spindle Torque: 188 ft. lbs.

Tools: 30

Table Load Capacity: 1540 lbs.

Rapid Traverse Rates (X & Y / Z): 590 / 472 IPM

Tool Change Time (T - T / C - C): 3.5 / 11 Seconds

Max Tool Diameter: 3.74" / 6.8"

Max Tool Length: 11.8"

Max Tool Weight: 26 lbs.

Machine Dimensions (L x W x H): 132.8" x 132.9" x 105"

Machine Weight: 14,991 lbs.

FEATURES:

YASNAC MX1 CNC CONTROL

9" Monochrome CRT

Table Chip Guards

Yellow Operation End Light

Two Gear Range Headstock

Heavy Duty Box Way Construction

$5000.00 Non Refundable Deposit Required Upon End of Auction

Balance Due By Cashiers Check Before Pick Up

Shipping Buyer is Responsible for All Freight & Rigging

Contact: Steve Norcio 410 750 1130

snorcio@mtacompanyinc.com